## Slide 1: PRESENTATION ON SOLAR COOKER MODELLING
NAME-ANSUMAN SADANGI(180301160029)
SOUNG SAMPURNA SWAIN(180301160027)
B.TECH MECHANICAL

## Slide 2: INTRODUCTION
A solar cooker is a device in which heat energy from sunlight is trapped inside the cooker using the phenomenon of the greenhouse effect. A solar heating device such as a solar cooker uses a reflector to reflect sunlight to a small area where the cooking container is placed.

## Slide 3: METHOD-
Incident sunlight reaching the parabolic dish is concentrated on the glass cover at the front face of the receiver. A first part of the concentrated solar radiation is reflected to the ambient, the glass absorbs a second part, and a third part is transmitted through the glass cover. The latter part is absorbed by the receiver plate. A small part is reflected back to the glass cover. Heat is transmitted to the fluid via the black-painted metal absorber. The selective coating layer has a high absorptance and a low emittance in order to reduce thermal radiation losses. Figure shows a cross section of the receiver and all heat transfer processes involved. The absorber is considered to be very rigid, and its properties are not affected by temperature.

## Slide 4: RESULTS-
The present model of the PSCS considers all the abovementioned heat transfer processes, takes into account the presence of the glazing on the receiver, and assumes one-dimensional variations of the temperature along the receiver and the storage tank. The first law of thermodynamics is applied between times t and t + Δt to various system components to obtain the governing energy balance equations in a convenient explicit finite difference form ready for numerical solution.

## Slide 5: EFFECT OF INSULATION THICKNESS
Heat losses must be carefully analyzed as their assessment can significantly affect the overall system performance accuracy. Thermal insulation of the receiver deserves a careful analysis as a thicker receiver wall reduces thermal losses but it increases the shadow area on the solar concentrator, as well as the receiver weight and system cost.
The receiver wall thermal resistance is the inverse of the global heat transfer coefficient resulting from conduction through the receiver and convection heat transfer on the interior and the exterior of the receiver.

## Slide 6: TYPES OF SOLAR COOKER
PANEL SOLAR COOKER
THE BOX SOLAR COOKER
PARABOLIC SOLAR COOKER
GOSUN SOLAR COOKER

## Slide 7: ABSTRACT
Several researchers have touched upon many aspects of the box cooker, but unfortunately an integrated image of the cooker has not emerged. The best example is the vessel, which hardly finds a mention in the entire literature. The performance of the conventional box-type solar cookers is appreciably improved, when detailed analysis of the heat transfer processes in a box cooker is identified and studied. This paper presents a mathematical model for a double-glazed hot-box type solar cooker loaded with conventional vessel on floor and another vessel having depressed lid on lugs, which enables to find the temperatures of various components of the cooker with time including vessel and its contents. The cooking vessel with depressed lid provides direct contact of the lid with the food and hence making the heat transfer more effective. This results in higher temperature of water/contents of cooking vessel in the cooking vessel with depressed lid compared to conventional vessel at the same time. The same trend is observed from the results.

## Slide 8: CONCLUSION
Heat losses must be carefully analyzed as their assessment can significantly affect the overall system performance accuracy. Thermal insulation of the receiver deserves a careful analysis as a thicker receiver wall reduces thermal losses but it increases the shadow area on the solar concentrator, as well as the receiver weight and system cost.
The receiver wall thermal resistance is the inverse of the global heat transfer coefficient resulting from conduction through the receiver and convection heat transfer on the interior and the exterior of the receiver.

## Slide 9: THANK YOU